## Slide 1
Service Oriented Architecture & SOME/IP Protocol
by,
G.Shiva Kumar

## Slide 2
AGENDA
What is Service Oriented Architecture
Service Oriented Architecture Example using SOME/IP
SOME/IP Protocol Introduction
SOME/IP Protocol Features
SOME/IP Service Interface & its elements
SOME/IP, SOME/IP-SD, SOME/IP -TP Message Formats
Pros and Cons of SOME/IP Protocol
SOME/IP Service Interface & Its Elements
Service Oriented Architecture
What is Service Oriented Architecture

## Slide 3
A Service Oriented architecture (SOA) is a Style of software design where services are provided to the other components by application components through a communication protocol over a network.
Communication , for which communication partners are generally not defined during design time , but dynamically discovered and bound during runtime.
Plug and play type communication
What is Service Oriented Architecture

## Slide 4
APP1
{
---------
---------
image_process( )
{
-----
-----
}
}
ECU-1
APP2
{
--------
--------
image_process( )
--------
--------
}
ECU-2
Provided service instance (DP)
(ip:127.0.0.1
Transport protocol: tcp/udp
Port:1400)
Required service instance
(DP)
SOME/IP
SOME/IP
Vehicle Ethernet Network
Multicast IP : 172.27.40.72
UDP Port: 1024
SERVICE INTERFACE_DP
{
Method : Image_process
Method Id: 272682
}
Required service found
Subscribe/acknowledgement
Call  image_process ( )
unsubscribe
Offer service()
find service()
Service Oriented Architecture Example

## Slide 5
SOME/IP is an Automotive/embedded Communication Protocol
SOME/IP Abbreviation is Scalable Service Oriented Middleware Over IP
Designed by BMW group 2011
SOME/IP is used for inter-ECU Client/Server Serialization
It relies on using Ethernet and TCP/IP
SOME/IP can be implemented on different Operating Systems(i.e. Autosar , GENIVI Linux and OSEK)
and Even Embedded Devices without Operating System.
SOME/IP Protocol Introduction

## Slide 6
7. SOME/IP Protocol comes under the session and presentation layer of OSI network Model and Responsible for the following operations like Session establishment , maintenance and termination , translation, Encryption /Decryption, Compression.
Application, presentation ,session layers
Transport Layer
Network Layer
Datalink Layer
Physical Layer
SOME/IP Protocol Introduction Continued ….

## Slide 7
SOME/IP Provides Service Oriented Communication over a Network.
SOME/IP Provides Wide range of middleware features
serialization – transforming into and from on-wire Representation.
Remote Procedure Call (RPC) – implementing Remote Invocation of functions
Segmentation of udp messages – allowing the transport of large SOME/IP Messages over udp without need of fragmentation.
Service Discovery (SD)
Service Discovery is used to explicitly signal:
Status of Service Instances (available or not) as well as how to reach the service
Publish/Subscribe : Which Events/Fields does a client need?
This state is transported using cyclic messages carrying entries: Service: Find, Offer , and
StopOffer , Eventgroup: Subscribe, StopSubscribe, SubscribeAck, and SubscribeNack.
SOME/IP Protocol Features

## Slide 8
Service interface :
Port Interface that consists of a heterogeneous collection of methods ,events and fields.
Service Interface Name
Methods
Events
method_name()
event_name
…
Fields
field name
event
get()
set()
…
…
Service Interface = Type of service provider consisting of
  Methods
  Events
  Fields
Server applications provide their data using a Service Interface Skeleton instance
Client applications use the server application by using a Service Interface Proxy instance
Proxys and Skeletons are transparently connected (intraprocess, interprocess, internetwork)
SOME/IP Service Interface & Its Elements

## Slide 9
Event :
A Uni-directional data transmission that is only invoked on changes or cyclically and is sent from producer of data to consumers
An Event Represents an update to a piece of data
Client
Server
X
inform
inform
inform
X=10
X=20
X=30
Here X is the Data provided by Server and Required by Client , client Subscribed to get the updates for x
SOME/IP Service Interface Element : Event

## Slide 10
Method :
A Method Represents a function that is executed by and in the scope of server on request od one or more Client(s).
Types of Method.
  With response(Request/Response).
  Without Response (Fire & Forget).
SOME/IP Service Interface Element : Method

## Slide 11
Field :
A Field represents a Piece of data hosted by a server that is accessible to one or more client(s)
Via get and/or set accessors.
Elements of a Field
  Setter (Method to set field value).
  Getter (Method to set field value).
  Notifier (Event to inform the new values on change of the field).
SOME/IP Service Interface Element : Method

## Slide 12: Events vs Fields

## Slide 13: SOME/IP Message Format

## Slide 14: SOME/IP Message Elements
Message ID [32 Bit]:
The message id is a 32 bit identifier that is used to identify the RPC call to a method of an application or to identify an event.
Structure of Message ID:
Length [32 Bit]:
Length field shall contain the length in Byte starting from Request ID/Client ID until the end of the SOME/IP Message.
Request ID [32 Bit]:
The Request ID allows a provider and Subscriber to differentiate multiple parallel uses of the same metod ,event, getter or setter.
The Client ID is the unique identifier for the calling client inside the ECU . The Client ID allows an ECU to Differentiate calls from multiple clients to the same method.
The session ID is a Unique identifier chosen by the Subscribers for each call . The Session ID allows a Subscriber to differentiate multiple calls to the same method.

## Slide 15: SOME/IP Message Elements Continued …
Protocol Version [8 Bit]:
Protocol Version shall be an 8 bit Field containing the SOME/IP protocol version.
Interface Version [8 Bit]:
Interface Version Shall be an 8bit field that contains the Version of the Service Interface
Message Type [8 Bit]:
The Message Type field is used to differentiate different types of messages and shall contain the following values as shown in Table

## Slide 16: SOME/IP Message Elements Continued …
Return Code [8 Bit]:
The Return Code Shall be UINT8 and used to signal whether a request was Successfully processed.
For Simplification of the header layout , every message transports the field Return code as 0X00.

## Slide 17: SOME/IP Message Elements Continued …
Payload:
The size of the SOME/IP payload field depends on the transport protocol used.
With UDP the SOME/IP Payload shall be between 0 to 1400 bytes.
The limitation to 1400 bytes is needed in order to allow for future changes to protocol stack.
Since TCP Supports Segmentation of Payloads , larger sizes are automatically Supported.

## Slide 18: SOME/IP-SD Message Format & its Elements.
When SOME/IP-SD find or offer service instances or handles subscriptions this is done by so called entries , which are transported in the entry array of the SOME/IP-SD Message

## Slide 19: SOME/IP-TP Message Format
The UDP binding of SOME/IP can only transport SOME/IP messages that fit directly into an IP packet. If larger SOME/IP messages need to be transported over UDP (e.g. of 32 KB) the SOME/IP Transport Protocol (SOME/IP-TP) shall be used.

## Slide 20: SOME/IP Pros & Cons
Pros and Cons
SOME/IP Supports a high data rate.
SOME/IP has low transportation overhead.
The initiation time of SOME/IP is notably short.
SOME/IP Suitable for driver assistance and infotainment systems.
Simple, better maintainability, and modular design.
But still complex for hard real time systems like motor control or brakes.

## Slide 21
Thank you